## Slide 1
Dr. Gaurav Bansod
Department of Electronics and Telecommunications
Pune Institute of Computer Technology, Pune,
Maharashtra, India.
IoT Security: Problems, Challenges and Solutions

## Slide 2
What is Cryptography ?
Encryption Process :
Transforming data
Using the algorithm
To make it unreadable to anyone
Except those possessing the key
Kerckhoff’s Principle : (1883)
A cryptosystem should be secure even if the attackers knows all the details about the system with exception of the secret key.

## Slide 3
What is Encryption System?
Insecure Channel
E
D
X
X
Y
Y
K
K
Secure Channel
Hacker
Y

## Slide 4
Lightweight Cryptography ?
It endorses algorithms which are best suited for constrained environment
For e.g. RFID Tags, sensors, contactless smart card, health-care devices and so on.
GE’S should be less than 2200.
Lightweight Cryptography
Heavy Security Algorithm

## Slide 5
Constrains
GE’s
Memory Requirement
Power Consumption
Throughput
Security
Parameters in Lightweight Cryptography

## Slide 6
Classification
Security
Cryptology
Cryptography Cryptanalysis
Symmetric Key Asymmetric Key
Block Cipher Stream Cipher

## Slide 7
Stream Cipher Vs Block Cipher
Stream Cipher
Pseudo Random bits are used for encryption and decryption
Practical Issue: Can generate the pseudorandom bits offline and decrypt very quickly without buffering.
E.g. Linear Feedback Shift Register (LFSR) but not secure.
Block Cipher:
Main goal of these ciphers are Security.
Permutation can be happened in Block cipher.
Permutation can be possible in Block Cipher which gives more diffusion layer.
E.g. AES, DES, PRESENT, FeW, etc.

## Slide 8
Block Ciphers
The Block Ciphers are further classified into three types i.e. Feistel Structure , SP Network and Generalized Feistel Structure.
Feistel Structure

## Slide 9
SP Network

## Slide 10
Generalized Feistel Structure

## Slide 11
Algorithms | Block Size | Key Size | Structure | GE's | Memory (Bytes) | Power (mW)
PRESENT | 64 | 128 | SPN | 1339 | 2756 | 38
SIMON | 64 | 128 | Feistel | 954 | 2324 | 35
SPECK | 64 | 128 | Feistel | 996 | 2310 | 31
LED | 64 | 128 | SPN | 1265 | 3876 | 100
Rectangle | 64 | 128 | SPN | 1787 | 2372 | 31
CLEFIA | 64 | 128 | GFN | 2488 | 4708 | 
Existing Block Ciphers
Table gives the some important parameter comparison for existing block ciphers.

## Slide 12
Main Blocks In Cipher Designs
There are some blocks which are required to design the Ciphers. E.g. S – Box, X – Or, Block Permutation, Bit permutation and Shifting.
1) S – Box
X | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
S(x) | 3 | F | E | 1 | 0 | A | 5 | 8 | C | 4 | B | 2 | 9 | 7 | 6 | D
4 bit S-Box
0 hex
3 hex
Binary 0 0 0 0
Binary 0 0 1 1

## Slide 13
2) Bit Permutation
X | 0 | 1 | 2 | 3
P(X) | 2 | 3 | 0 | 1
e hex
3 hex
Binary 1 1 1 0
Binary 1 0 1 1
4 bit P-layer

## Slide 14
3) Block Permutation
12345678 hex
34127856 hex
1 2 3 4 5 6 7 8
3 4 1 2 7 8 5 6

## Slide 15
4) Circular Shifting (Left shift by 2)
F |  |  |  | 2 |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0
E |  |  |  | 5 |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
C |  |  |  | B |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 1

## Slide 16
5) X - OR
1 0 1 0
0 1 0 1
1 1 1 1
Why Only X – OR is used in design why not AND, OR …… ?
1 | 0 | 1 | 0 | Plain Text
0 | 1 | 0 | 1 | Key
1 | 1 | 1 | 1 | Cipher Tex
1 | 1 | 1 | 1 | Cipher Text
0 | 1 | 0 | 1 | Key
1 | 0 | 1 | 0 | Plain Text
Encryption
Decryption

## Slide 17
AND Gate and OR Gate Explanation
1 | 0 | 1 | 0 | Plain Text
0 | 1 | 0 | 1 | Key
0 | 0 | 0 | 0 | Cipher Tex
AND
Encryption
Decryption
0 | 0 | 0 | 0 | Cipher Text
0 | 1 | 0 | 1 | Key
0 | 1 | 0 | 1 | Plain Text
AND
1 | 0 | 1 | 0 | Plain Text
0 | 1 | 0 | 1 | Key
1 | 1 | 1 | 1 | Cipher Tex
OR
Encryption
Decryption
1 | 1 | 1 | 1 | Cipher Text
0 | 1 | 0 | 1 | Key
1 | 1 | 1 | 1 | Plain Text
OR

## Slide 18
Existing Cipher Designs Till date
1) PRESENT (An ISO Certified Cipher)
PRESETN is an ISO certified SP Network

## Slide 19
2) BORON (SP Network)

## Slide 20
3) ANU (Feistel Structure)

## Slide 21
4) LBlock (Feistel Structure)

## Slide 22
5) CLEFIA (Generalized Feistel Structure)

## Slide 23
6) PICCOLO (Generalized Feistel Structure)

## Slide 24
Merits and Demerits of SP, Feistel and GFS
SP Network
SP Network has very strong in terms of security
It uses 64 bit of permutation so throughput is less
It requires more GE’s
Feistel Structure
Due to the use of block shuffling it has high throughput
Requires les number of GE’s as compared to other networks
Gives best security
Due to data divide uses less memory
Generalized Feistel Structure
It has more throughput
It has less memory requirement
Due to number of blocks the key scheduling is also divided
Might be gives low security assurance.

## Slide 25
Input and Key
X - OR
……………………………
P63 P1 P0
64 Bit Plain Text
K127 …………… K1 K0
128 Bit Key
From that take only 64 bit key as per key scheduling algorithm
Design Box
……………………………
……………………………
C63 C1 C0
64 Bit Cipher Text
Rotate Same Round

## Slide 26
How Key is Generated?
……………………………
K128 K1 K0
128 Bit Plain Text
Key Scheduling Algorithm
……………………………
K128 K1 K0
Rotate Same Round
After applying key scheduling algorithm we can use 64 bit, 32 bit or 16 bit key from 128 bit key which is based on your design.

## Slide 27
Key Scheduling Algorithm
……………………………
K128 K1 K0
128 Bit Key
left circular shift by 13
……………………………
K128 K1 K0
Apply S – box on left most 8 bit
……………………………
Add Round Counter
……………………………
Rotate Same Round
Extract 128 bit, 64 bit, 32 bit or 16 bit Key as per your design

## Slide 28: Structure

## Slide 29
How to make Design Lightweight ?
Memory Aspect:
Reduce the number of the variable in code
Use maximum local variables
Use the functions which help to reduce the code size
Power Aspect:
Power is controlled by use of minimum rounds but security should not be compromised
GE’s
Use minimum number of S – Boxes because it requires GE’s
Use minimum number of X – OR operations
Use more number of permutations because permutation doesn’t require GE’s but with increasing in permutation throughput gets increased

## Slide 30
Blocks which require GE’s
Mainly the GE’s are required for the S – Box, Storing Element and X – Or.
A3 | A2 | A1 | A0 | B3 | B2 | B1 | B0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1) S - Box
K – Map
Can Calculate other equitation's also by using the K – Map
AND, OR and NOT require physical memory to store the bits.
One 4 bit S – Box requires 28 GEs

## Slide 31
2) X - OR
X – Or requires data register to store the bit so it requires 2 GE’s
3) Bit Permutation, Block Permutation and Shifting
Bit permutation, Block permutation and circular shifting doesn’t requires GE’s. It requires only wires so use of permutation and shifting will save the GE.
ASIC Technology Table
For calculation of GE we used standard library of IBM 8RF with 0.13um technology.
Gates | No. of GE’s
NOT | 0.75
AND | 1.25
OR | 1.25
XOR | 2.00
2:1 MUX | 2.25
D flip flop | 4.25

## Slide 32
64 Bit data register = 64*4.25 = 272 GE
No GE Required
Approximately for 4 bit S – Box 28GE are required = 28*8 = 224
Approximately for 4 bit S – Box 28GE are required = 28*8 = 224
For X – Or 2 GE’s are required = 32*2 =64
For X – Or 2 GE’s are required = 32*2 =64
Complete Key scheduling algorithm requires 500GE’s
No GE Required

## Slide 33
Main Objective
Constrains
GE’s
Memory Requirement
Power Consumption
Throughput
Security

## Slide 34
Why we used 64 bit plain Text and 128 bit Key ?
1) Brute Force Attack
By taking A to Z letters with each combinations :
26 * 25 * 24 * ……..*1 = 26 ! = 2 ^ 88 = 2 ^ 56 * 2^ 32
A cubana Machine can find the data of 2^56 in one day so for other 2^32 data it requires some years nearly equal to 99 years.
So we used large key space i.e. 128 bit key.